## Slide 1: networking
Network “Big Stack”
Instructor:
Dr. Rick Gibson

## Slide 2: OSI Reference Model - History
“Open System Interconnect” Model
An Early attempt to have HW / SW manufacturers agree on a Networking FW
Late 1970’s (2 Independent but Related Projects):
  ISO
  CCITT (International Telegraph/Telephone Consultative Committee)
Each defined Similar Models
1983 – both documents were “Merged”
  “Basic Reference Model for Open Systems Interconnection”
    Later, simply, “OSI Model”
1984 – Published by ISO & CCITT (now renamed ITU)
  ISO 7498 for the ISO side
  X.200 for the ITU Side
    Model specified its own set of related Protocols (“OSI Protocol Suite”), but its Implementation did not “catch on”
TCP/IP Did “Catch On”
  Became the “Basis” of the Internet
  REFERENCE: http://www.tcpipguide.com/free/t_HistoryoftheOSIReferenceModel.htm

## Slide 3: Layer Function Summary
Lower Layers (“Bottom Half”):
  1 – Physical
  2 – Data Link
  3 - Network
  4 – Transport
    FYI – VPNs fully encrypt the Lower Half
Upper Layers (“Top Half”):
  5 - Session
  6 - Presentation
  7 – Application Interface
    REFERENCE: http://www.tcpipguide.com/free/t_OSIReferenceModelLayerSummary.htm
      MOST Encryption is in the Top Half

## Slide 4: Layer Function Summary …
Physical:
  Encoding & Signaling
    “Serializing” Parallel (inside of computer) into Serial (on Media)
    Physical Data Transmission
    OUTPUT called “Frames”:
      Contains ALL contributions (layer-protocols) from all participating higher Layers

## Slide 5: Layer Function Summary …
Data Link
  Establishes Coarse Framing Control for Physical Layer
  HW Addressing
  2 Sub-Layers:
    Logical Link Control (LLC) on top:
      Data Framing Construction / Regulation
        IEEE Project 802
      LAN versus WAN Protocol Definitions
    Media Access Control (MAC) on bottom:
      Communication Rules for specific Media Types
      HW / MAC address of the NIC is defined here

## Slide 6: Layer Function Summary …
LLC’s Project 802 “LAN/MAN Standards” Summary:
  802.1
    Higher-Layer LAN Protocols Working Group
      LAN/MAN Architecture
      WAN Architecture
      Security
    Bridging Standards
    802.Q
      Trunk-ing for VLANs
    802.1P
      QoS Traffic Prioritization
    802.1X
      Port-Based Network Access Control
        Standard for Authenticating devices at the Data Link Level
        Devices must first Authenticate using the Extensible Authentication Protocol EAP
  802.2 = LLC = DISBANDED
  802.3
    Ethernet Working Group
  802.4 = Token Bus = DISBANDED
  802.5 = Token Ring = DISBANDED
  802.6 = MANs = DISBANDED

## Slide 7: Layer Function Summary …
  802.7 = Broadband LAN using Coax = DISBANDED
  802.8 = Fiber Optic = DISBANDED
  802.9 = Integrated Services LAN (ISLAN or isoETHERNET) = DISBANDED
  802.10 = Interoperable LAN Security = DISBANDED
  802.11
    Wireless LAN (WLAN) & Mesh (Wi-Fi)
  802.12 = 100BaseVG = DISBANDED
  802.13 = Unused
  802.14 = Cable Modems = DISBANDED
  802.15 = Wireless PAN = DISBANDED
  802.15.1
    Bluetooth
      (more at Reference Link)
        REFERENCE: https://en.wikipedia.org/wiki/IEEE_802
  802.16 = Wireless WAN

## Slide 8: Layer Function Summary …
Network:
  Logical Addressing (SW Address) – “Long Distance Addressing” = IP
  Routing
  Fragmentation & Reassembly
    According to rules of Layer 2 Link MTUs
  Routers Devices work at this Layer

## Slide 9: Layer Function Summary …
Transport:
  Connections
    Comm Handshake called – TCP 3-way Handshake
  Segmentation & Reassembly
  Acknowledgements & Retransmission
    Guaranteed Delivery of data
    “Counting Numbers” for each SEGMENT (L4 buffer) Sent
  Flow Control

## Slide 10: Layer Function Summary …
Session:
  Definition:
    A Semi-Permanent…
    Interactive…
    Information Interchange, also known as a:
      Dialogue
      Conversation
      Meeting
    … between:
      two or more communicating devices
      between a computer and user
  Session Establishment, Management and Termination

## Slide 11: Layer Function Summary …
Presentation:
  Data Translation, as needed
    Formatting data for proper Presentation
  [Data Compression]
  [Data Encryption] = SSL => TLS

## Slide 12: Layer Function Summary …
Application Interface:
  (largest number of protocols in this Layer)
  Provides “User Application Services” available to any Network

## Slide 13: OSI mapping to TCP/IP (“ATIN” / DOD) Model
Application Interface :
  Layer 7
  Layer 6
  Layer 5
Transport
  Layer 4
Internetworking (Internet)
  Layer 3
Network Interface (NIC)
  Layer 2
  Layer 1

## Slide 14: TCP/IP History
TCP/IP protocols
  1969
    Initially developed as part of the research network developed by the United States Defense Advanced Research Projects Agency (DARPA or ARPA)
    Became “ARPAnet”
  1973
    Development of a full-fledged system of internetworking protocols for the ARPAnet began
      Spring of 73
        Network Control Program (NCP) by Vinton Cerf
      Summer 1973 Cerf and Vinton started working on a replacement
    1 core protocol – TCP
      Originally, “Transmission Control Program”
        Later became TCP with the publication of RFC 675 in December 1974

## Slide 15: TCP/IP History …
Original TCP was doing too much of the work
  Split into 2 parts, forming a Protocol Suite :
    TCP above
    IP below
      Suite Standardized in 1982
1/1/1983 – ARPAnet switched from NCP to TCP/IP
ARPAnet ceased to exist in 1990
  “Internet” took its place
Additional Protocols “Evolved into existence”

## Slide 16: Application Layer Protocol History …
Telnet – 1969
  “Teletype Network” – RFC 19
  Officially “standardized”
    March 5 , 1973
    “Teletype over Network Protocol” – RFC 206
  Port 23
FTP
  RFC 114 in 1971
  Ports 20,21
TFTP – 1980

## Slide 17: Application Layer Protocol History …
SMTP
  Early protocols (1971)
    Mail Box Protocol
    SNDMSG Program
    RFC 788 – 1981
  Port 25 (Unencrypted), 465 (Encrypted)
POP3 – Post Office Protocol
  Original Release (POP) in 1984, the upgraded to POP2 in 1985, followed by POP3 in 1988
  Port 110 (Unencrypted), Port 995 (Encrypted)
IMAP – Internet Message Access Protocol
  Designed by Mark Crispin in 1986 as a remote access mailbox protocol, in contrast to the widely used POP
  Port 143 (Unencrypted), Port 993 (Encrypted)

## Slide 18: Application Layer Protocol History …
DNS
  Dates back to SRI-NIC implementation of the ultimate “Hosts.txt” file
    Downloaded by users usually daily
    Updates were made manually to this global, file
    Port 53
  RFC 883 – 1983
BOOTP
  Ports 67, 68
  RFC 851 – 1985
DHCP
  Based on BOOTP
  Ports 67, 68 (the BOOTP ports)
  RFC 1531 - 1993
SNMP
  V1 series – 1988
  V2 series – RFC 1213 – 1991
  Ports 161 (Message Traffic) and 162 (SNMPTRAP)

## Slide 19: Application Layer Protocol History …
NBNS
  NetBIOS (WINS in Microsoft)
    Developed by Sytek Inc. in 1983 to be used in IBM’s PC LAN Network
    1987 – NetBIOS over TCP/IP
      RFC 1001
  NBNS grew as a SERVICE using RFC 1001
  Ports 137, 138
HTTP
  Tim Berners Lee (CERN) first proposed - 1989:
    HTML
    HTTP
    WWW
  Port 80 (Unencrypted), Port 443 (Encrypted)
  V0.9 (1 command = “GET”) – 1991
  V1.0 – RFC 1945 - 1996
  V1.1 – RFC 2068 - January 1997

## Slide 20
App. Interf.
SMTP
SNMP
NNTP
ftp
telnet
http
bootp
NFS
DNS
WINS
Presentation
Session
SMB
Transport
TCP
Segment
UDP
Datagram
Network
LLC
MAC –
Physical
IP Packets / Datagrams
ICMP
EGP
SLIP
ARP
DLC
SDLC
HDLC
NetBEUI
MS
TCP/IP
IBM
Legend:
DHCP
Project 802
Framing
Custom
LDAP
https
Routers
Repeators / Hubs
A
T
I
N
RIP, OSPF
ATM
FR
Broad
SONET
SDH
X.25
WAN Protos
(Circuit Switching)
LAN Protos
(Packet Switching)
ETH
TR
FDDI
NBNS
VoIP
DLL
DOD
cache
Sockets
NAT
Browser
SAMBA
mpls
HW
RDR.SYS
SRV.SYS
Transport Driver Interface TDI
NetBIOS
LDAPS
ftps
ssh
DRV
PORTS
ISAKMP
“Secy. Assn. Svc.
EAP/EAPOL
Custom Authentication
Above the Net Stack
PAP/
CHAP
HW
SW
Wi
Max
WL
IPSEC
ESP
AH
IGMP
RS-232
GRE
PPTP
L2TP
TLS
SSL
BGP
.onion
ISO/OSI Model
L2TP
PPP
PEAP
Cisco
LEAP
Bridges/
Switches
secy
L2F
(Packet Switching)
PORTS
TOR
Browser

## Slide 21
Extranet
To Biz Partners
Network/s
B2B
DMZ -“Perimeter”
Edge Router
(BGP)
/
FW
FW / BGP / NAT
IGRP or
VPN
FW
FW
RADIUS/
TACACS/
Diameter
SW
SW
SW
SW
VPN
DIRECTORY
Logon
Proxy
DFW
R
Branch
R
Corp
FW
Intranet
WWW
DBMS
[FW]
BGP
Azure
AWS
Extranet
To Biz Partners
Network/s
Extranet
To Biz Partners
Network/s
Google
10/24
R
VPN
Honey
Federation
SSO
FW
Remote
Client
Public
Email
Bastion –
Limited DNS
Proxy,
VPN,
Honeypot
Public-
Facing
WWW
Federation
SSO
DNS
Public-Facing
Resources
Sub Nets
Scanning /
Legitimacy
Sub Net
NIDS
/ NIPS
NAC /
Health
Intranet
Internet
VPN

## Slide 22
App.
Presentation
Session
Transport
Network
LLC
MAC –
Physical
Port /Prot
FW
GW
(VPN)
Switches
Repeators / Hubs
Bridges
Proxy
NAT
Routers
Routers
Routers
destination
Switches
Routers
Hops
DLL
QoS
OS
sw
Rtr
NLB
IDS
/IPS
SF FW
Next Gen
ML/AI
Picky
Routers

## Slide 23
.
–
Copyright IQ Consulting Services 2008
23
FireWall
GateWay
Switches
Proxy
Routers
Routers
Routers
destination
Switches
Routers
Hops
MGT
Control
Plane
NOS
sw
Rtr
Forwarding / Data
Plane
OF
Northbound
E_W Interface
APP
southbound
SDN Model
APP
APP
“Switching
Fabric”

## Slide 24: L2TP Framing

## Slide 25
Hyper-V (NEW)
O/S
(Core, No GUI mgt. Tools)
O/S
(Core, No GUI mgt. Tools)
Child partition
VM
With a Guest and
Services / Apps
Parent
O/S for comm with
Hyper V
Hardware
O/S
(Core, No GUI mgt. Tools)
O/S
(Core, No GUI mgt. Tools)
O/S
(Core, No GUI mgt. Tools)
O/S
(Core, No GUI mgt. Tools)
The mapping between:
The VM
  Has a virtual NIC
Uses which physical NIC on a host
Virtual
Switch
Virtual
Storage
Controller
Virtual
NIC
Intra-net
Q
FIFO

## Slide 26
UPD
HOSTS
HOSTS
HOSTS
HOSTS
HOSTS
HOSTS
HOSTS
HOSTS
HOSTS
HOSTS
HOSTS
HOSTS
SC/VMM
FABRIC
{100% IP on your part}
P-Net
XYZ Cloud
P-Store
Library
HOSTS
Abstraction of :
Templates
Profiles